## Slide 1
Structural and Shape Reconstruction using Inverse Problems and Machine Learning Techniques with Application to Hydrocarbon Reservoirs
PhD Viva
PhD Candidate: Clement Oku Etienam
Internal Examiner: Dr Nan Zhang
External Examiner: Dr Piroska Lorinczi

## Slide 2: Introduction
Talk Overview
Background Knowledge
History Matching with Level set
Electromagnetic History Matching
4D Seismic History Matching
History Matching with Machine Learning
Conclusion
References

## Slide 3
Background Knowledge

## Slide 4: Background
History matching
Inverse Problem: given specific observations (i.e.: real pressure & production data), infer information about model parameters (porosity & permeability).
The number of observations are finite and the data always contains measurement errors.
Constraining the outputs from a reservoir simulator (i.e.: simulated pressure & production data) by changing the uncertain model parameters to mimic the observations is known as History matching.
  Maintain geological realism.
  Be conceptually understandable to the user and management given a reasonable amount of training.
  Have predictive power not just in terms of matching future field production but in terms of the physics of the system.

## Slide 5: Workflow: Introduction
Geomechanics, Faults,
CO2 Capture & Storage
NEW 3D Property map
PRIOR. DATA (well logs, core analysis, petrophysics, PVT...)
4D seismic (A)
COST FUNCTION
- EnKF & ES
- Adjoint Technique
INVERSE PROBLEM
HISTORY MATCHING
A=f(P, Sw, …)
low frequency EM (H):
SATURATION INVERSION
( = g(Sw,..))
+
SHAPE Evolution
K (mD) from 4D seismic
PRODUCTION DATA
Fluid flow eq.
+
- ES-MDA
Geostatistics
PRODUCTION DATA
MPS

## Slide 6: 3D Forward Problem. 3 phase fluid flow in porous media
Darcy velocity of each phase,
indicates the quantities relating to oil, water and gas respectively
=
effective porosity, and =phase saturation and phase pressure, relative permeability. =absolute permeability, =phase relative permeability, =phase density, = phase viscosity, =phase formation volume factor. =source and sink terms representing the phase production and injection. =solution gas-oil ratio, =oil-water capillary pressure , = gas-oil capillary pressure. =vertical coordinate (height) and =magnitude of the gravitational acceleration.
,
Craft, B. C. & Hawkins, M., 1991. Applied Petroleum Reservoir Engineering. .:Prentice Hall.

## Slide 7
: Saturations
: Pressures
K
: Absolute permeability
: Production Rates (DATA)
Q=
=1
MPS or SGS
EM(7th year)
Q =-
= = )gh
MPS or SGS
Crichlow, H. B., 1977. MODERN RESERVOIR ENGINEERING-A Simulation Approach. 1st ed. Oklahoma: Prentice-Hall, Inc. Englewood Cliffs, New Jersey 07632
= effective porosity
3D Forward Problem. 2 phase fluid flow in porous media

## Slide 8: Forward problem, Maxwell Equation
: Conductivity
: Permittivity
: Permeability
E: Electric field
H: Magnetic field
J: Electric Current
M: Magnetic current
Finite difference Frequency domain
O Dorn, H Bertete-Aguirre and G C Papanicolaou,2007, Adjoint fields and sensitivities for 3D electromagnetic
imaging in isotropic and anisotropic media,, in: Lecture notes in Mathematics, Vol 1943/2008 ‘Inverse Problems
and Imaging’, pp 35-65, Springer Berlin/Heidelberg
Conductivity Estimation

## Slide 9: Forward problem Reservoir monitoring from low frequency Electromagnetic (EM) Data. 1KHz
Condutivity Estimation

## Slide 10: Inverse Problem: History matching
,
,
There exists an orthogonal matrix , an orthogonal matrix and an matrix such that
Where with .
Simulated
Observed
Goal:
min

## Slide 11
Sequential statistical Monte Carlo method (Derived from Kalman Filter)
Representation of error statistics by an ensemble of model states
  Mean and covariance
Evolution of error statistics by ensemble integrations
  Stochastic model equation
  Bayesian style sequential data assimilation( time-dependent)
Assimilation of measurements using a variance minimizing update
  Sequential updating of both model state and static parameters
  Model state and parameters converge towards true values
  Information accumulates and uncertainty is reduced at each update
Evensen G, et al 2007. Using the EnKF for assisted history matching of a north sea reservoir model. SPE Reservoir simulation symposium, Volume 1, pp. SPE 89942-PA.
Ensemble Kalman Filter

## Slide 12: EnKF state-space parameter (model states)
=ensemble of state and parameters,=absolute permeability,=effective porosity,
=Botom-hole presure of injector well , =pressure,
=water production rate, =saturation
=oil production rate, j=1,..ensemble members(100), k=time-step period, i=gridblock index(pixel).
hyp= Any hyper-parameter to be updated , =model parameters, =model states, =simulated data
Ensemble Kalman Filter

## Slide 13: Ensemble Kalman Filter data assimilation (real-time inversion)
=Prior ensemble , =covariance matrix of ensemble
=Kalman gain matrix , =Ensemble members(100), j=1,…
=Observed data( Qoil, Qwater, Pressure( Sw if EM assimilated). =Gaussian error
=Analysed ensemble of perm and poro, =information matrix
=covariance matrix of error in observed data
Ensemble Kalman Filter

## Slide 14
Lidar and Digital Outcrop Modelling(DOM) to get TI’s
Lidar: A laser-based measurement system that captures an outcrop geometry
in 3 dimensions (point cloud)
DOM: A spatially constrained, 3D digital MAP of an outcrop built by projecting digital
imagery onto a lidar point cloud derived mesh
Burton, D., D.B. Dunlap, L.J. Wood, & P.P. Flaig, 2011, Lidar intensity as a remote sensor of rock properties, Journal of Sedimentary Research, v. 81, n. 5, p. 339- 347. DOI: 10.2110/jsr.2011.31.

## Slide 15: Bayesian Formulation Framework for Uncertainty Quantification
Tarantola, 2005. Inverse problem theory and methods for model parameter estimation. 1 ed. Philadelphia: SIAM

## Slide 16: Ensemble Based Optimization Ensemble Smoother Multiple Data Assimilation ES-MDA
is the estimated covariance between the forecast models and forecast data and is the auto covariance of predicted data.
=data assimilation times
From Bayesian formulation
(2013) Ensemble Smoother with Multiple Data Assimilation, Emerick A A., &Reynolds A..:. Computers & Geosciences , 55(11), pp. 3-15

## Slide 17: ES-MDA, Continued
Algorithm : ES-MDA
Choose the number of data assimilations, and the coefficients for For Run the ensemble from time zero For each ensemble member, perturb the observation vector using , where Update the ensemble using, end(for)
Algorithm : ES-MDA
(2013) Ensemble Smoother with Multiple Data Assimilation, Emerick A A., &Reynolds A..:. Computers & Geosciences , 55(11), pp. 3-15

## Slide 18: Inverse problem Non-Linear Kaczmarz for EM inversion to conductivity(off-line)
ADJOINT MAXWELL MODEL
Low Frequency EM inversion
: Conductivity
: Complex conjugate of
Ej(x): Electric Field
Update term
(Adjoint of Linearised residual operator)

## Slide 19: Inverse problem Non-Linear Kaczmarz for EM inversion to conductivity(off-line)
Sweep_loop: DO
Source_loop: DO
END DO source_loop
END DO sweep_loop
Low Frequency EM inversion

## Slide 20: Inverse problem. Archie Equation
=scaled water conductivity(Siemens/m) given by IJWC equation , (Report and Dresser, 1982)
= effective porosity, = water saturation distribution, =temperature of injected water in Celsius
, , = constants specified in Archie(1942), Hils &Milburn(1956), = salt concentration in ppm
= conductivity (Siemens/m)
Water saturation from conductivity

## Slide 21: Gaspari-Cohn 5th order compact support
Covariance Localisation Matrix
Update Equation becomes,
Acting on the permeability and porosity pixel update
= correlation matrix, z=Euclidean distance to well location, c=correlation length

## Slide 22: Sparse Representation of Model Space
OMP is a greedy algorithm for obtaining a sparse representation of the model parameters X using this over-complete dictionary.
Combine K-SVD and Orthogonal Matching Pursuit (OMP) for reducing the dimension of the model space (regularization)
(2006) An Algorithm for Designing Overcomplete Dictionaries for Sparse Representation K-SVD, Aharon M., Elad M. & Bruckstein A..:. IEEE Transactions on Signal Processing, 54(11), pp. 4311-4322.
Reduce computational complexity and enforce prior information by representing the model by a sparse over-complete dictionary learned from the channelized initial ensemble
K-SVD is an unsupervised learning algorithm to create an over-complete dictionary.

## Slide 23: Compressed sensing K-SVD/OMP
Dictionary creation )
D
Y
t
X
Initial ensemble geostatistic
Target: Dictionary
From K-SVD
Target: Sparse signal from OMP
[ncells : n_ini_realizations]
[ncells : nkcluster_realizations]
=
[nkcluster_realizations
: nkcluster_realizations]
Step 1: K means clustering to select atoms (D)
Step 2: freeze D and update X with OMP
Step 3: freeze X and update D with K_SVD

## Slide 24: Compressed Sensing, Continued K-SVD
Replace unused atom with minimally represented signal
Identify signals that use k-th atom (non zero entries in rows of X)
Deselect k-th atom from dictionary
Find coding error matrix of these signals
Minimize this error matrix with rank-1 approximation from SVD
[U,S,V] = svd(Ek)
Replace coefficient of atom dk in X with entries of s1v1
dk = u1/u12
Initialize Dictionary
Sparse Coding
(OMP)
Update Dictionary
One atom at a time

## Slide 25: Compressed Sensing, Continued Orthogonal Matching Pursuit(OMP)
Select dk with max
projection on residue
xk = arg min ||Y-Dkxk||
Update residue
r = Y - Dkxk
Check terminating
condition
D, Y
x

## Slide 26: K-SVD with OMP
For a set of training signals , find the elements which are necessary to construct a dictionary from K-SVD.
Find a sparse combination of elements of D representing each vector of the training set of signals
The corresponding weights of the signals describing are denoted as . They are calculated by solving the optimisation problem,
(2006) An Algorithm for Designing Overcomplete Dictionaries for Sparse Representation K-SVD, Aharon M., Elad M. & Bruckstein A..:. IEEE Transactions on Signal Processing, 54(11), pp. 4311-4322.

## Slide 27: Root Mean Square Error (RMSE)
: Number of data assimilation time steps where measurements are assimilated (measurement times)
: Number of data collected at each time step
: Ensemble member index
: Time index
: Metric or response (history matched metric or response)
: Observed data metric for metrics j (Data equivalent in state space ensemble) at time step k.
: Simulated data from simulator for metrics j (Data equivalent in state space ensemble) at time step
k.
: Observed data standard deviation for metrics j (Data equivalent in state space ensemble).
Quality measure
Production data misfit

## Slide 28
History Matching with Level set

## Slide 29: Heaviside Function, Narrow-Band Schematic and signed distance transformation
Level Set
Heaviside representation of K
Equivalent Narrow-band map
Equivalent signed distance representation

## Slide 30: Inverse problem. EnKF-Level-set coupling
=
=Narrow-band function (matrix of 0’s and 1’s)
EnKF-Issues with Computational time!
EnKF- Level Set
Heaviside function ( and )
Signe distance function
Assimilated Ensemble state
Initial Ensemble state (with Level Set)

## Slide 31: Numerical results Result of Level-set implementation
(a) & (d) True permeability field , (b) Model recovered with EnKF-Level set(c) SSIM map of EnKF-Level set,(e) Model recovered by EnKF, and (f) SSIM map of EnKF
(a) (b) (C) (d) (e) (f)

## Slide 32
Electromagnetic History
Matching

## Slide 33: Electromagnetic History Matching
Stochastic Realisations
Objective function
Pressure-Production data
EnKF
Assimilation using Level set
conductivity
IF EM data is available, include
Conductivity estimation EM (Maxwell Equation)
ELSE
Reservoir Simulator
Stopping
criterion
Reached?
No
Yes/Stop
Data to be assimilated
Forecast ensemble
Well logs
Outcrop
Seismic survey
Initial ensemble (100 realizations)

## Slide 34: Inverse problem EnKF-Level-set coupling( with EM assimilation) and covariance localization
=Narrow-band function acts on the level set functions
EnKF- Level Set- EM

## Slide 35: Gaussian reservoir synthetic model
Property | Value
Grid configuration | 84
Grid size | 100
Well configuration | 2-spot( Line-spot)
Producers | 1
Injectors | 1
Simulation period | 8 yrs
Reservoir depth | 4000ft
Integrated data | Injectors BHP, producers oil and water rates, water saturation distribution(7th year only)
Injectors constraint | 15,000 to10,000( bbl./day)
Producer constraint (BHP) | Constant 140psi
Ensemble size. Number of realizations | 100
Uncertain parameter to estimate | Permeability, porosity, Sw
Number of integration steps | 16
Property | Value
Grid configuration | 
Grid size | 
Well configuration | 2-spot( Line-spot)
Producers | 1
Injectors | 1
Simulation period | 8 yrs
Reservoir depth | 4000ft
Integrated data | Injectors BHP, producers oil and water rates, water saturation distribution(7th year only)
Injectors constraint | 15,000 to10,000( bbl./day)
Producer constraint (BHP) | Constant 140psi
Ensemble size. Number of realizations | 100
Uncertain parameter to estimate | Permeability, porosity, Sw
Number of integration steps | 16

## Slide 36: Reference permeability model for Electromagnetic HM experiment
(a) 3D permeability field of the true Gaussian synthetic model showing the two well locations and (b) 2D permeability field of the true Gaussian synthetic model showing the two well locations
(a)
(b)

## Slide 37: Numerical Results Conductivity reconstructed from Low-frequency EM data
(a) (b)
2D-view conductivity plume: (a) True water conductivity distribution of the reference/true reservoir, (b) Reconstructed conductivity profile

## Slide 38: Numerical Results Conductivity reconstructed from Low-frequency EM data

## Slide 39: Numerical Results Water saturation inferred from conductivity
(a) (b)
(a) Reconstructed conductivity profile, (b) Equivalent water saturation distribution of the reconstructed conductivity profile using Archie’s law.

## Slide 40: Covariance Localisation Matrix
(a) (b) (c)
(a) Correlation function from 5th order Gaspari –Cohn matrix, (b) Correlation function (sensitivity functions) from our non-linear Kazsmarz solver and (c) Correlation function arriving from the combination of both approaches

## Slide 41: RMS Evolution of EM inversion to Conductivity
(A)-RMS evolution during the conductivity reconstruction of the EM data from the sources to receivers.
(B)-RMS function evolution of the reconstructed conductivity profile.

## Slide 42: production-data response

## Slide 43: production-data response Cont’d

## Slide 44: Numerical Results Water-saturation reconstruction from numerical experiments
(a) (b) (c) (d)
Water saturation reconstruction of the various methods. (a) Initial model water saturation, (b) Water saturation recovered by EnKF (d) Water saturation distribution recovered from EnKF-EM and (d) True model water saturation distribution reconstructed from kazsmarz method

## Slide 45: Numerical Results Water-saturation reconstruction from numerical experiments-3D view
3D Water saturation reconstruction of the various methods. (a) Initial model water saturation, (b) Water saturation recovered by EnKF (d) Water saturation distribution recovered from EnKF-EM and (d) True model water saturation distribution reconstructed from kazsmarz method

## Slide 46: Numerical Results Permeability reconstruction from numerical experiments
(A) (B) (C) (D)
permeability reconstruction from the various methods. (a) Initial permeability model, (b) permeability recovered by EnKF (c) permeability recovered from EnKF-EM and (d) True model permeability field

## Slide 47: Numerical Results RMSE Evolution
Realizations | Initial model | RMS value with EM data assimilation | RMS data without EM data assimilation
45 | 67.34 | 20.24 | 15.31
34 | 52.74 | 10.34 | 7.34
67 | 122.45 | 9.38 | 8.96
85 | 45.22 | 7.45 | 4.43
24 | 36.31 | 6.42 | 1.67

## Slide 48
4D Seismic History
Matching

## Slide 49: 4D Seismic History Matching
Compartmentalized reservoirs require understanding of fault dynamics on reservoir management, performance and overall economics,
Fault Transmissibility Multipliers (FTM) are commonly applied in the representation of faults and their effects on production in reservoir simulation.
An absolute multiplier (FTM) is generally applied, and subsequently altered on a trial and error basis, with geological input when available. [Manzocchi et al., 2002].
The acquisition of extensive petrophysical hard data (core samples) from faults is impractical and the traditional estimation of FTM from petrophysical parameters only provides static and local information.

## Slide 50
is the absolute transmissibility multiplier applied in order to represent the effect of fault rock between grid-blocks.
is the absolute transmissibility multiplier in each cell.
= 2-phase transmissibility multiplier(updated from 4D seismic)
k1,2 : grid-block permeability
L1,2 : grid-block length
tf : fault thickness
Multi-Phase Fault Transmissibility Multiplier(FTM)
(Manzocchi, et al., 2002)

## Slide 51
Previous Work
In this work FTM are estimated trough quantitative integration of time-lapse data using EnKF.
Mahmood, I. & Villegas, R., 2016. History Matching of Reservoirs by Updating Fault Properties and Rock-fluid Properties Using 4D Seismic Results. Conference Proceeding. EAGE, 78 International Conference & Exhibition, Vienna
4D Seismic Data
Macbeth, et al., 2006
Gassmann., 1951
Sw inversion
Sw i
Fault Analysis
Pseudo rel. perm curves
Generate initial ensemble of
FTM values to be used in EnKF loop

## Slide 52
Determine 2-phase FTM value
The first step was to make the simulator treat the reservoir zone, and the fault zone as separate distinct regions.
Assign separate relative permeability properties for the fault zone based on data from literature on fault core analysis. Synthetic capillary pressure curves based on literature data following Ringrose’s relation and assigned to the fault
Zone grid-blocks.
Mahmood, I. & Villegas, R., 2016. History Matching of Reservoirs by Updating Fault Properties and Rock-fluid Properties Using 4D Seismic Results. Conference Proceeding. EAGE, 78 International Conference & Exhibition, Vienna
Previous Work

## Slide 53
Determine 2-phase FTM value
Reservoir zone and Fault zone grid-blocks assigned as separate regions in simulation
Fault zone grid-blocks assigned separate relative permeability properties based on laboratory core analysis results (Knipe et al. 1997, Al-Hinai et al. 2006)
Synthetic Pc curves generated
Sw from seismic used to create pseudo-relative permeability curves and two-phase FTM
Mahmood, I. & Villegas, R., 2016. History Matching of Reservoirs by Updating Fault Properties and Rock-fluid Properties Using 4D Seismic Results. Conference Proceeding. EAGE, 78 International Conference & Exhibition, Vienna
Previous Work

## Slide 54
Objectives
Given the time-lapse impedance maps and Sw (water saturation) inversion outputs
For the initial Deterministic case determine the 2-phase Fault transmissibility multiplier from prior work
Generate an ensemble of permeability and porosity fields using the sequential Gaussian simulation (SGS)
Generate an ensemble of FTM values initially estimated with
4D seismic
Without 4D seismic
History matching the simulation model by using the Ensemble Kalman filter and Levenberg Marquadt procedure(deterministic case) to update the absolute permeability, effective porosity and FTM values
Generate synthetic impedance maps using the Gassmann equations to qualitatively compare simulation results to the real model.
Compare production data matches using Root-mean-square Function and Impedance map reconstruction using structural similarity index metric (SSIM)

## Slide 55
Workflow
4D Seismic Data
Macbeth, et al., 2006
Gassmann., 1951
Sw inversion
Sw i
Fault Analysis
Pseudo rel. perm curves
SGS
Parametrisation of permeability, porosity and FTM
Initial ensemble of FTM values(with and without 4D seismic results)
Objective Function
Generate initial ensemble of
FTM values to be used in EnKF loop
EnKF
Yes/Stop
Stopping
criterion
Reached?
No
3D images instead
3D images instead
3D images instead

## Slide 56
Simulation Model
Depth (ft)
Compartment 1
Compartment 2
y – directional Fault

## Slide 57
Numerical Experiments
Model | 4D-seismic | FTM value | Mode
LM- 2 phase FTM | Yes | 0.0039 | Deterministic
EnKF-no-FTM | No | 0.002 | Stochastic
EnKF-FTM | No | 0.056 | Stochastic
EnKF-2 phase FTM | Yes | 0.0043 | Stochastic
absolute permeability ensemble
= porosity ensemble

## Slide 58
Results
Slide 58
3D Fault model of the EnKF -2 phase FTM scheme
FTM

## Slide 59
Results
(A-E) Permeability for the true model, (F-J) final permeability for the EnKF-FTM model without 4D seismic, and (K-O) final permeability for the 3D EnKF No-FTM with 4D seismic
EnKF (without 4D seismic)
EnKF (K only)
True model
EnKF (K, FTM)

## Slide 60
Results
(A-E) Permeability for the true model, (F-J) final permeability for the EnKF-2phase FTM model with 4D seismic, and (K-O) final permeability for the 3D LM-2phase FTM model with 4D seismic
EnKF vs Gradient method (with 4D seismic)
True model
EnKF (K & FTM4D)
LM (K & FTM4D)

## Slide 61
Result
Comparison between the History matched models of the EnKF-FTM, EnKF-2 phase FTM, EnKF No-FTM and LM-2 phase FTM: (a) oil production rate profile, (b) water production rate profile and (c) injection pressure profile
(a) (b) (c)

## Slide 62
Results
RMS values
Model | 4D Seismic | RMS value
EnKF-FTM | No | 4.97
EnKF-2 phase FTM | Yes | 2.98
EnKF-No FTM | No | 5.26
LM-2 phase FTM | Yes | 9.64

## Slide 63
Results
Synthetic Impedance map
Forward modelling of rock and fluid physics relationships enables the expression of seismic attributes(acoustic impedance), as a function of reservoir properties such as fluid saturation.
Mahmood, I. & Villegas, R., 2016. History Matching of Reservoirs by Updating Fault Properties and Rock-fluid Properties Using 4D Seismic Results. Conference Proceeding. EAGE, 78 International Conference & Exhibition, Vienna

## Slide 64
Results
Reconstructed Impedance images
True
EnKF-2 phase-FTM
EnKF-FTM
EnKF-No-FTM
LM-2 phase-FTM

## Slide 65
Results
Structural Similarity Index Metric(SSIM)
We use SSIM to compare the EnKF-FTM, EnKF-2 phase FTM, EnKF No-FTM and LM-2 phase FTM final impedance maps of the history matched models. SSIM is an image quality metric that assesses the visual impact of three characteristics of an image: luminance, contrast, and structure (, and ). A value of 1 describes complete similarity, 0 describes no similarity and a value of indicate complete dissimilarity. The overall index mathematically is a multiplicative combination of the three terms. (Wang, et al., 2004)
We derive our SSIM Normalized cost function as,
……(13)
…..(14)

## Slide 66
Results
Overall cost function comparison
Experimental Model | SSIM | SSIM Normalised Cost Function | RMS Function | Overall Cost Function
EnKF-FTM | 0.7645 | 0.2355 | 4.97 | 2.603
EnKF-2phase FTM | 0.8522 | 0.1478 | 2.98 | 1.5639
EnKF-No FTM | 0.7480 | 0.252 | 5.26 | 2.756
LM 2-phase FTM | 0.8715 | 0.1285 | 9.64 | 4.884

## Slide 67
Conclusions
Multi-phase properties of relative fault transmissibility multipliers results in a closer and lower RMS function.
Impedance maps generated for the two-phase FTM’s result in a close visual match to true.
The LM-2phase FTM model(from prior work) produce a good impedance map reconstruction, however this method was inferior to the EnKF scheme in terms of 2-Norm comparison
EnKF yielded a lower RMS function when compared to prior deterministic method
Assimilating more data during the EnKF inversion scheme leads to a reduced RMS function value to the pressure-production historical data
Future work is to apply a sparse history matching modulation using orthogonal matching pursuit with 4D seismic(on-going work )

## Slide 68
History Matching with Machine Learning

## Slide 69: Workflow: Sparsity-accelerated structural stochastic optimization
Input to geostatistic:
Training image & prior data
Multiple Point Statistic (MPS)
K-means& K-SVD (Done off-line and once)
Forward Problem
Initial ensemble =
Reservoir simulator
Forecast
Over-complete K-SVD Dictionary =
Sparse Domain, permeability ensemble
Inverse Problem
ES-MDA
Production data
Ensemble Smoother Multiple Data Assimilation (ES-MDA):
Analysed ensemble
ii) Recover spatial analysed ensemble
iii) End iteration if convergence reached
Select 100 Realizations
Learned Dictionary used in OMP
Initial learning ensemble =
OMP algorithm, convert to sparse domain
=cov()
= cov(,
=cov(error())
Notes: ncells x n_fin_realizations

## Slide 70: Sparsity promoting History Matching
Novel History Matching Technique, Coupling,:
ES-MDA
WITH
K-SVD/OMP Unsupervised Dictionary Learning

## Slide 71: Numerical Experiments/Results for Sparse HM
Observed Data
  4 producer well :Oil rate, water rate, GOR.
  4 Water injector wells : Bottom hole pressure
Initial ensemble
  100 Models
  Porosity and permeability (36,000 active grid blocks
Data Assimilation with ES-MDA

## Slide 72: Numerical Experiments/Results for Sparse HM Over-Complete Learned Dictionary from K-SVD
Four selected members of the dictionary
………out of 1500
Layers 1-5

## Slide 73: Numerical Experiments/Results for Sparse HM Permeability Reconstruction
Initial ES-MDA
ES-MDA & Sparsity
True
Visual comparison. Layers 1-5

## Slide 74: Numerical Experiments/Results Permeability Reconstruction
Initial
ES-MDA & Sparsity
True
ES-MDA
Visual comparison. Layer 1

## Slide 75: Numerical Results for sparse HM RMSE Evolution
Realisations | Initial model | ES-MDA | ES-MDA+K-SVD model
47 | 58.34 | 24.24 | 15.31
31 | 52.74 | 10.34 | 10.34
63 | 122.45 | 9.38 | 8.96
86 | 35.22 | 7.45 | 4.43
23 | 36.31 | 9.42 | 0.32

## Slide 76: Numerical Experiments/Results for sparse HM Production data match
Initial ensemble
History matched ensemble. ES-MDA & K-SVD/OMP

## Slide 77: Conclusions
ES-MDA can efficiently history match complex reservoir models
  General tool for parameter and/or state estimation.
  Practically no restrictions on parameter space.
  Problem with local minima reduced.
Updated ensemble provides future prediction with uncertainty estimates
History matching with Machine Learning Techniques gave lower RMS data match and reasonable permeability reconstruction
The model space was reduced leading to a better-posed inverse problem

## Slide 78: References
(2012) Sparse geologic dictionaries for subsurface flow model calibration: Part 1, Inversion formulation, Khaninezhad, M. M., Jafarpour, B. & Li, L., 2012.. Advances in Water Resources, 39(1), pp. 106-121.
(2008) History matching of petroleum reservoirs using a level set technique, Dorn O & Villegas R, INVERSE PROBLEMS Volume: 24 Issue: 3 Article Number: 035015 Published: JUN 2008.
(2006) An Algorithm for Designing Overcomplete Dictionaries for Sparse Representation K-SVD, Aharon M., Elad M. & Bruckstein A..:. IEEE Transactions on Signal Processing, 54(11), pp. 4311-4322.
(2017) History Matching of Reservoirs by Updating Fault Properties Using 4D Seismic Results and Ensemble Kalman Filter, Etienam C, Intesar M & Villegas R , SPE Europec featured at 79th EAGE Conference and Exhibition, Paris, SPE-185780-MS (22pp.).
(2013) Ensemble Smoother with Multiple Data Assimilation, Emerick A A., &Reynolds A..:. Computers & Geosciences , 55(11), pp. 3-15
(2007) Signal recovery from random measurements via orthogonal matching pursuit. Tropp, J. A. & Gilbert, C. A. Information Theory.,,IEEE Transactions on, 53(12), pp. 4655-4666.
(2016) Integrated Structural Reconstruction and History Matching Using Ensemble Filter and Low-frequency Electromagnetic Data. C. Etienam, R. Villegas & M. Babaei. EAGE conference proceeding. EAGE-SPE Annual Conference & Exhibition, Vienna, Austria, June 2016.

## Slide 79: References Con’td
(2017) History Matching of Reservoirs by Updating Fault Properties using 4D Seismic Results and Ensemble Kalman Filter. C. Etienam, I. Mahmood and R. Villegas. SPE paper SPE-185780-MS. 79th EAGE-SPE Annual Conference & Exhibition, France, 12-15 June 2017.
(2018) CO2 Sequestration Using Ensemble Kalman Filter and Considering a Sustainability Approach. R. Villegas, C. Etienam, F. Rahma. SPE paper SPE-185780-MS. 80th EAGE-SPE Annual Conference & Exhibition, Copenhagen, 11-14 June 2018.
(2018) Shape and Distributed Parameter Estimation for History Matching using a Modified Ensemble Kalman Filter and Level Sets. ; R. Villegas , C. Etienam, O. Dorn and M Babaei . Submitted to Inverse problems.
(2018) An Enhanced Water-Flooding History Matching Scheme Incorporating Electromagnetics:, C. Etienam, R. Villegas , M. Babaei and O. Dorn, SIAM ,Erlangen, Germany
(2018) An Improved Reservoir Model Calibration using Sparsity and Stochastic Optimization. C. Etienam, R. Villegas , and O. Dorn. ECMI, Budapest, Hungary.
(2009) The Ensemble Kalman Filter in Reservoir Engineering--a Review . S. Aanonsen, , D. Oliver ,A. Reynolds, & B. Vall, . SPE Journal, 14(3), pp. 393-412.

## Slide 80: References Con’td
(2009) Evensen, G., 2009. Data Assimilation, The Ensemble Kalman filter. 2nd ed. Berlin: Springer.
(1951) Gassmann, F., 1951. Uber die elastizitat poroser medien: Vierteljahrss-chrift der naturforschenden gesellschaft in Zurich.
(1997) Lia, O. et al., 1997. Uncertainties in reservoir production forecasts. AAPG Bulletin, Issue 81, pp. 775-801.
(2006) Macbeth, C., Floricich, M. & Soldo, J., 2006. Going quantitative with 4D seismic analysis. Geophysical Prospecting, Volume 54, pp. 303-317.
(2016) Mahmood, I. & Villegas, R., 2016. History Matching of Reservoirs by Updating Fault Properties and Rock-fluid Properties Using 4D Seismic Results. Conference Proceeding. EAGE, 78 International Conference & Exhibition, Vienna
(2002) Manzocchi, T., Heath, A., Walsh, J. J. & Childs, C., 2002. The representation of two phase fault-rock properties in flow simulation models. Petroleum Geoscience, Volume 8, pp. 119-132.
(1999) Manzocchi, T., Walsh, J., P. Neil & Yielding, G., 1999. Fault transmissibility multipliers for flow simulation models. Petroleum Geoscience, Volume 5, pp. 53-63.
(2009) Villegas, R., Fisher, Q. 2009. Optimizing fluid-rock properties in compartmentalized reservoirs by using 4D Seismic Data. 2nd International Conference on Faults and Top Seals, Montpelier.
(2004) Wang, Z., Bovik, A. C., Sheikh, H. R. & Simoncelli, E. P., 2004. Image quality assessment: from error visibility to structural similarity. Image processing IEEE Transactions, 13(4), pp. 600-612

## Slide 81: Acknowledgement
I will like to thank the Niger Delta Development Commission of Nigeria (NDDC) of the Federal Republic of Nigeria for sponsoring my PhD Program

## Slide 82: Thank you for your attention
Comments and questions?